NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED FRUNTZ TO THE INSIDE OF VEHICLE AS SHOWN BELOW.

- DRILL 4 No 8mm DIAMETER HOLES AS INDICATED APPROX 25mm UP FROM THE BOTTOM OF THE CAB VALANCE.

- USING NUTS AND BOLTS SUPPLIED, SECURE FRUNTZ SECTION INTO POSITION.

- WITH SELF-TAPPER PROVIDED SECURE BOTTOM FRONT SECTION BY STEP (SEE DIAGRAMME).

- OFFER UP REAR SECTION AND DRILL 2 No 8mm DIAMETER HOLES AS INDICATED 25mm IN FROM EDGE OF WING, GETTING POSITION 6 AS LOW AS POSSIBLE.

- USING NUTS AND BOLTS PROVIDED, SECURE REAR SECTION IN PLACE.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.DAF.04

DAF 75

SLEEPER

FITTING

INSTRUCTIONS

1. 8mm HOLE DRILLED 25mm IN FROM BACK OF FRUNTZ.

2 & 3. DRILLED AT TOP OF CURVES.

4. 375mm UP FROM BOTTOM OF SPATZ

THIS SHOWS A BOLT BUT A SELF TAPPER ON TO INNER PANEL IS NOW SUPPLIED

5. 125mm DOWN FROM CURVE IN CHASSIS WING.

6.AS LOW AS POSSIBLE.