NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED KITZ FORWARD SECTION TO THE INSIDE OF CAB MUDGUARD AS SHOWN BELOW.

- DRILL 3 NO 8mm DIAMETER HOLES AS INDICATED BELOW, (POSITIONS 1,2 & 3) 25mm INTO VEHICLE MUDGUARD PANEL THROUGH THE VEHICLE MUDGUARD AND THE KITZ FLANGE.

- BOLT FRONT SECTION INTO PLACE WITH NUTS AND BOLTS SUPPLIED.

- OFFER UP REAR SECTION OF KITZ. DEPENDING ON VEHICLE THIS SECTION MAY HAVE TO BE TRIMMED ALONG ITS BOTTOM EDGE TO ACHIEVE CORRECT ALIGNMENT WITH THE BOTTOM OF THE FRONT SECTION.

- DRILL 3 NO 8mm HOLES EVENLY SPACED, (POSITIONS 4,5 & 6) AS SHOWN BELOW.

- BOLT REAR SECTION INTO PLACE USING NUTS AND BOLTS SUPPLIED.

PAINT BOLT HEADS IF REQUIRED. ANY TRIMMING NECESSARY COULD BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# KTZ.IVC.04

IVECO EUROTECH

SUPER KITZ

FITTING INSTRUCTIONS

## SPATZ-SHOP

SALES LINE

01527 60606

1. 8mm HOLE 35mm UP FROM STEP IN CAB VALENCE.     BE ACCURATE

2. 8mm HOLE 45mm IN FRONT OF JOINT.

3. 8mm HOLE 75mm IN FROM BACK END OF KITZ.

4. 50mm DOWN FROM STEP IN CHASSIS WING.

5. CENTRAL POSITION BETWEEN 4 & 6.

6. 75mm UP FROM BOTTOM OF KITZ REAR SECTION