NOTE. CARE MUST BE TAKEN IN THE POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS STRONGLY RECOMMENDED.

- CLAMP CORRECTLY SIDED FRUNTZ TO THE INSIDE OF VEHICLE AS SHOWN BELOW.

- DRILL 2 No. 8mm DIAMETER HOLES APPROX 30mm UP FROM THE BOTTOM OF THE CAB VALANCE (POSITIONS 1&2) AND ONE 8mm DIAMETER HOLE 40mm INTO CAB VALANCE AS SHOWN BELOW (POSITION 4).

- USE SHORTER LENGTH BOLTS (20mm) IN POSITIONS 1&2 AND LONGER BOLTS IN POSITION 3 (35mm).

- OFFER FRUNTZ REAR SECTIONS TO INSIDE OF VEHICLE AS SHOWN BELOW. ADJUST TO LINE UP WITH FRUNTZ SECTION. CLAMP INTO POSITION.

- WITH CAB TILTED OR FRUNTZ SECTION REMOVED, DRILL 3No 8mm HOLES 4,5 AND 6 AS SHOWN 25mm INTO VEHICLE MUDGUARD AND BOLT INTO PLACE.

NOTE. WE HAVE NOTICED THAT SOME CUSTOMERS HAVE USED SPEED CLIPS TO FIX FRONT SECTION TO AVOID DRILLING VEHICLE.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

SPATZ SHOP

PHONE

NUMBER

01527 60606

# KTZ.VOL.D4

VOLVO FM DAY

FITTING

INSTRUCTIONS

1. 8mm HOLE DRILLED 70mm IN FROM BACK OF FRUNTZ.

2. 8mm HOLE DRILLED 240mm IN FRONT OF CAB JOINT. 30mm UP.

3. 8mm HLOE DRILLED 75mm UP FROM BOTTOM OF FRUNTZ. 40mm INTO CAB VALANCE. GREAT CARE SHOULD BE TAKEN DRILLING THIS POSITION. A PILOT HOLE IS STRONGLY ADVISED. ONCE DRILLED, REMOVE FRUNTZ AND SEE LOCATION HOLE IN FLANGE.

4.UNDER FRUNTZ SECTION. 50mm ABOVE TOP CREASE IN REAR PART OF MUDWING

5. APPROX 300mm ABOVE POSITION 6

6. 50mm UP FROM BOTTOM OF KITZ REAR SECTION