NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED FRUNTZ TO THE INSIDE OF THE VEHICLE AS SHOWN BELOW.

- DRILL 3 No. 7mm DIAMETER HOLES APPROX 25mm UP INTO THE CAB VALANCE AS SHOWN.

- USING THE NUTS AND BOLTS SUPPLIED, SECURE FRONT SECTION INTO POSITION.

- OFFER FRUNTZ REAR SECTION UP TO THE INSIDE OF THE VEHICLE AS SHOWN BELOW. ADJUST TO LINE UP WITH FRONT SECTION.

- DRILL 2 No. 7mm HOLES, 4 & 5, AS SHOWN 20mm INTO THE VEHICLE MUD- GUARD AND BOLT INTO PLACE.

ANY TRIMMING CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.DAF.01

DAF 55/65

DAY CAB

KITZ FITTING INSTRUCTIONS

5. 100mm UP ABOVE BOTTOM OF REAR SECTION

4. 45mm DOWN BELOW CREASE LINE

3. 80mm IN FROM BACK

2. LOCATED AT CORNER.

1. 90mm UP FROM BOTTOM OF FRUNTZ.