NOTE: CARE SHOULD BE TAKEN IN POSITIOING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED KITZ FORWARD SECTION TO THE OUTSIDE OF CAB MUDGUARD AS SHOWN BELOW.

- DRILL 3 No. 8mm DIAMETER HOLES AS INDICATED BELOW, CENTRALY IN FLANGE THROUGH THE VEHICLE MUDGUARDS AND KITZ FLANGE.

- USING NUTS AND BOLTS, SECURE FRUNTZ SECTION INTO POSITION.

- OFFER UP REAR SECTION OF KITZ.

- DRILL 3 No 8mm HOLES AS SHOWN BELOW.

- USING NUTS AND BOLTS, SECURE REAR SECTION INTO POSITION.

ANY TRIMMING NECESSARY CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.DAF.06

DAF 95 SLEEPER

FITTING INSTRUCTIONS

2. 8mm HOLE 400mm FROM POSITION 1.

1. 8mm HOLE 200mm UP FROM BOTTOM OF KITZ.

4. 8mm HOLE 50mm FROM BACK END OF KITZ.

5. 8mm HOLE 50mm DOWN FROM STEP ON BACK SECTION.

6. 8mm HOLE LOCATION OF YOUR CHOICE.

7. 8mm HOLE 50mm UP FROM BOTTOM OF KITZ REAR SECTION.

3. 50mm DOWN FROM TOP OF WING.