- IT IS ADVISABLE TO CLEAN OUT AND LUBRICATE THE PRE-THREADED HOLES ON THE INSIDE OF THE CAB VALANCE PRIOR TO THE FITTING OF SPATZ.

- CLAMP CORRECTLY SIDED KITZ FRONT SECTION TO THE INSIDE OF THE CAB VALENCE AS SHOWN BELOW. NOTE. ON SOME VEHICLES, THERE IS A STABILISING BRACKET AT POSITION 6 WHICH, IF FITTED WILL HAVE TO BE UNFASTENED AT THE CAB VALANCE END PRIOR TO FITMENT OF THE KITZ (T30 TORQUE SCREW).

- USING THE BOLTS AND WASHERS PROVIDED, BOLT KITZ FRONT SECTION IN PLACE, AND DO NOT OVER TIGHTEN. (IT MAY BE NECESSARY TO ELONGATE SOME OF THE PRE-DRILLED HOLES IN KITZ FRONT SECTION).

IF DESIRED, THE TORQUE SCREW AT POSITION 6 CAN BE REUSED, CLAMPING THE KITZ FRONT SECTION BETWEEN THE BRACKET AND VEHICLE.

- OFFER KITZ REAR SECTION UP AS SHOWN TO LINE UP WITH FRONT SECTION.

- DRILL 3No. 8mm HOLES THROUGH VEHICLE CHASSIS WING AND KITZ REAR SECTION FLANGE AS DETAILED BELOW.

- BOLT INTO PLACE USING NUTS AND BOLTS SUPPLIED.

- ANY TRIMMING REQUIRED, CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

SPATZ SHOP

SALES LINE

01527 60606

# KTZ.DAF.07

DAF 95 & 105XF

KITZ FITTING INSTRUCTIONS

75mm UP FROM BOTTOM OF CHASSIS WING

120mm BELOW CHASSIS WING CREASE

50mm ABOVE CHASSIS WING CREASE

USE CAPTIVATED NUT ON INSIDE OF CAB WING