- CLAMP CORRECTLY SIDED KITZ FRONT SECTION TO THE INSIDE OF CAB MUDGUARD AS SHOWN.

- DRILL 4, 3mm PILOT HOLES AS SHOWN THROUGH VEHICLE MUDGUARD AND KITZ FORWARD SECTION 25mm FROM INNER EDGE OF VEHICLE MUDWING.

- CHECK HOLE POSITIONS, IF OK OPEN HOLES UP WITH A 8mm DRILL.

- USING NUTS AND BOLTS, SECURE FRONT SECTION IN TO PLACE.

- OFFER UP REAR SECTION, DRILL THREE HOLES 5,6 AND 7 AS SHOWN. REPEATING STEPS 2 AND 3.

- USING NUTS AND BOLTS, SECURE REAR SECTION IN TO PLACE.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

KTZ.DAF.D3

DAF 85 DAY CAB

TIPPER

FRUNTZ KITZ

FITTING INSTRUCTIONS

SPATZ SHOP SALES LINE 01527 60606

HOLES 2 & 3 DRILL EVENLY SPACED BETWEEN 1 & 2.

HOLE 1 DRILL 50mm UP FROM BOTTOM OF WING.

HOLE 4 DRILL 50mm IN FROM REAR OF WING.

HOLES 5,6 & 7 DRILL EVENLY SPACED.