NOTE: - FIT SPRAY SUPPRESSION SHIELD FIRST.

- CLAMP CORRECTLY SIDED LOGO FRUNTZ FORWARD SECTION TO THE INSIDE OF CAB MUDGUARD AND SPRAY DEFLECTION SHIELD AS SHOWN BELOW.

- TO FIT SPRAY SHIELD (SEE SEPARATE SHEET). DRILL 3 NO 10mm DIAMETER HOLES AS INDICATED BELOW, POSITIONS 4, 5 & 6, 30mm INTO VEHICLE MUDGUARD PANEL, THROUGH BOTH VEHICLE MUDGUARD AND THE FRUNTZ FLANGE. DRILL A FOURTH HOLE THROUGH THE VEHICLE, THE SPRAY DEFLECTION SHIELD AND THE FRUNTZ FLANGE. (POSITION 3).

- REMOVE FRUNTZ AND PUT A 9mm 120 STUD (LONGEST) THROUGH EACH OF THE 4 No HOLES IN THE CAB VALANCE RETAINING WITH A PLASTIC WASHER.

(NOTE: EXTRA PLASTIC WASHERS MAY BE REQUIRED TO TAKE UP PLAY).

- ENLARGE HOLES IN FRUNTZ FLANGE TO 12mm.

- USING A FASTENER RECEPTACLE AS A TEMPLATE, DRILL 1 No. 3mm HOLE ON EACH SIDE OF THE FOUR 12mm DIAMETER HOLE IN THE FRUNTZ FLANGE.

- FIX EACH RECEPTACLE TO THE BACK OF THE FRUNTZ FLANGE USING 2 No. 3mm X 10mm STEEL POP RIVETS.

- OFFER FRUNTZ UP TO VEHICLE AND SECURE BY TURNING EACH OF THE QUARTER TURN PANEX FASTENERS UNTIL LOCKED.

- OFFER REAR SECTION UP TO VEHICLE AND CLAMP INTO POSITION.

- DRILL 3 HOLES (POSITIONS 7,8 & 9) REPEATING STEPS 2 TO 7.

CHECK CLEARANCE BETWEEN FRONT SECTION AND TONGUE OF REAR, ANY TRIMMING NECESSARY CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

KTZ.IVC.05

IVECO EUROSTAR

FRUNTZ KITZ

ITZ

SPATZ SHOP SALES LINE 01527 60606

3. HORIZONTALLY IN LINE WITH STEP IN FRUNTZ 30mm INTO VEHICLE.

4. 30mm FORWARD OF FRUNTZ CORNER (DOOR OPEN)

5. CENTRAL.

6. 60mm IN FROM BACK END OF FRUNTZ.

7. 50mm DOWN FROM STEP IN CHASSIS WING.

8. CENTRAL BETWEEN 7 & 9

9. 65mm UP FROM BOTTOM OF FRUNTZ