NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

LEFT HAND SIDE FIRST

- OFFER UP MAIN SECTION SLIDING IN BETWEEN OUTER CAB WING AND UNDER WHEEL ARCH MUDWING SHIELD AS SHOWN BELOW.

- DRILL 3 No. 8mm DIAMETER HOLES AS INDICATED BELOW, (POSITIONS 1, 2 & 3) 35mm INTO VEHICLE MUDGUARD AND THE KITZ FLANGE.

- BOLT FRONT SECTION INTO PLACE WITH NUTS AND BOLTS SUPPLIED.

- OFFER REAR SECTION UP, DRILL 3 No. 8mm HOLES (POSITIONS 4, 5 & 6) AS SHOWN BELOW.

- BOLT REAR SECTION INTO PLACE USING NUTS AND BOLTS SUPPLIED.

PAINT BOLT HEADS IF REQUIRED. ANY TRIMMING CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

RIGHT HAND SIDE

- ON RIGHT HAND SIDE OFFER UP MAIN SECTION SLIDING IN BETWEEN OUTER CAB WING AND UNDER WHEEL ARCH MUDWING SHIELD AS SHOWN BELOW.

- DRILL 2No 8mm HOLES AS POTION 1 & 2 AND BOLT INTO PLACE.

- OPEN SIDE STOWAGE BOX AND USING METAL BRACING SUPPORT, DRILL 6mm HOLE IN FLOOR IN LATCH GAP BOLT IN PLACE POS 7, FIX REAR SPATZ TO EXTENDED METAL BRACKET USING THE NUTS AND BOLTS SUPPLIED POS 8.

- OFFER REAR SECTION UP, DRILL 3 No. 8mm HOLES (POSITIONS 4, 5 & 6) AS NEAR SIDE.

- BOLT REAR SECTION INTO PLACE USING NUTS AND BOLTS SUPPLIED.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.IVC.06

IVECO STRALIS

FITTING INSTRUCTIONS

5. CENTRAL POSITION BETWEEN 4 & 6.

4. 25mm UP FROM START OF OUTWARD RETURN

3. 8mm HOLE 50mm IN FROM BACK END OF KITZ.

2. 8mm HOLE 50mm IN FROM DOOR CREASE ON RIGHT

1. 8 mm HOLE

50 mm UP FROM BOTTOM OF KITZ

6. 75mm UP FROM BOTTOM OF KITZ REAR SECTION.

7. DRILL 6mm HOLE THROUGH FLOOR BETWEEN LATCH GAP, BOLT BRACKET TO UNDER SIDE.

8. DRILL 6mm HOLE THROUGH SPATZ FLANGE AND METAL BRACKET.

BOLT POSITIONS 1 AND 2.