NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED KITZ FRONT SECTION TO THE INSIDE OF CAB MUDGUARD AS SHOWN.

- BEFORE DRILLING, IN HOLE POSITION 3 THERE IS A BOLT THAT HOLDS THE TWO-WING SECTION TOGETHER THIS CAN BE USED TO SECURE SPATZ IF REQUIRED POSITION MARKED ON FLANGE OF SPATZ. IF NOT DRILL 4 NO 8mm HOLES AS SHOWN THROUGH THE VEHICLE MUDGUARD AND KITZ FORWARD SECTION, 25 mm UP INTO VEHICLE MUDGUARD.

- USING NUTS AND BOLTS PROVIDED, SECURE FRONT SECTION INTO POSITION.

- OFFER UP REAR SECTION AND CLAMP INTO POSITION.  CHECK CLEARANCE WITH FRONT SECTION ALLOWING FOR CAB MOVEMENT.  IT MAY BE NECESSARY TO EITHER TRIM OFF THE UNDERSIDE OF THE BACK SECTION TO LINE UP WITH THE UNDERSIDE OF THE FRONT SECTION OR ADJUST THE CHASSIS WING OUTWARD TO GAIN CLEARANCE & TYRE COVERAGE.

- DRILL 3 NO 8 mm HOLES AS SHOWN BELOW.

- USING NUTS AND BOLTS PROVIDED, SECURE REAR SECTION INTO POSITION.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.MAN.06

MAN TGA

M, L & LX

FRUNTZ KITZ

2. CENTRALLY BETWEEN 1 & 3

1. 80mm UP FROM BOTTOM OF WING

3. SEE OPTIONS ABOVE OR DRILL TO THE REAR OF BOLT MOUNTING BEHIND WING

4. 50mm FROM REAR OF SPATZ

5. CENTRALLY IN RECESS

6. CENTRALLY BETWEEN 5 & 6

7. 60mm UP FROM BOTTOM OF WING