NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED KITZ FRONT SECTION TO THE INSIDE OF THE CAB MUDGUARD AS SHOWN.

- DRILL 4 No. 8mm DIAMETER HOLES APPROX 30mm UP FROM THE EDGE OF CAB WING. POSITION 1 NEEDS TO BE 40mm UP FROM THE BOTTOM OF THE FRONT SECTION (SEE BELOW). POSITION 3 NEEDS TO BE 20mm TO THE REAR OF THE SPLIT IN THE CAB WING.  YOU CAN THEN MEASURE 350mm FORWARD AND REAR TO OBTAIN POSITIONS 2 & 3.

- USING NUTS AND BOLTS SUPPLIED FIX FRONT SECTION INTO POSITION.

- OFFER REAR SECTION UP AND DRILL 3No. 8mm HOLES 30mm IN FROM WING EDGE. POSITION 7 TO BE 50mm UP FROM BOTTOM OF REAR WING. (WITH CAB AT RIDE HEIGHT) POSITION 5 CAN BE MEASURED 250mm FROM LOCATION 4. POSITION 6 EQUALLY SPACED BETWEEN 5 & 7.

- USING NUTS AND BOLTS SUPPLIED FIX REAR SECTION INTO POSITION.

- ANY TRIMMING CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

SPATZ-SHOP PHONE NUMBER 01527 60606

KTZ.MAN.07

MAN TG-A

FITTING

INSTRUCTIONS

1. 40mm UP FROM  BOTTOM OF MUDGUARD.

2.350mm FROM POSITION 3

3. 20mm FROM REAR LINE OF SPLIT IN CAB WING.

4. 350mm FROM POSITION  3

5. MEASURE  250mm FROM POSITION 4.

6. EQUALLY SPACED BETWEEN 5 & 7

7. 50mm UP FROM BOTTOM      OF REAR SECTION