NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED MAIN KITZ SECTION (WITH LOGO) TO UNDERSIDE OF CAB AS SHOWN, TAKING CARE TO SLIDE THE KITZ FLANGE BEHIND THE VEHICLE INNER MOULDING BY FIXING POSITION 2.

- DRILL 3 No. 8mm DIAMETER HOLES THROUGH VEHICLE WING AND KITZ FLANGE AS SHOWN BELOW. (SEE 1,2 & 3)

- FIX SECTION INTO POSITION USING NUTS AND BOLTS SUPPLIED.

- OFFER UP KITZ FRONT SECTION AND REPEAT STEP 2. (SEE 4,5 & 6).

- OFFER UP REAR SECTION AND SLIDE UP AND DOWN FOR BEST FIT.

- FOLLOWING STEP 2, SECURE REAR SECTION WITH NUTS AND BOLTS. (7,8 & 9).

PAINT FASTENINGS BOLTS AS REQUIRED, ANY TRIMMING NECESSARY CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.MER.A5

ACTROS

MEGA SPACE

FRUNTZ KITZ

2. 225mm UP FROM BOTTOM OF CAB DOOR. 35mm UP INTO VEHICLE.

1. 40mm IN FROM BACK OF MAIN SECTION. 35mm INTO VEHICLE.

3. CENTRALLY BETWEEN 1 & 2, 35mm UP INTO VEHICLE.

7. 50mm DOWN. 35mm INTO WING.

4. 100mm BELOW BOTTOM OF CAB DOOR. 20mm FROM WING EDGE.

5. 50mm DOWN FROM TOP OF FRONT SECTION. 40mm FROM WING EDGE.

6. 50mm UP FROM BOTTOM OF FRONT SECTION. 40mm FROM WING EDGE.

8. MIDWAY BETWEEN 7 & 9 AND 35mm INTO WING.

9. 25mm UP FROM BOTTOM OF REAR SECTION. 35mm INTO WING.