NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED MAIN KITZ SECTION (WITH LOGO) TO UNDERSIDE OF CAB AS SHOWN, TAKING CARE TO SLIDE THE KITZ FLANGE BEHIND THE VEHICLE INNER MOULDING BY FIXING POSITION 2.

- DRILL 2 No. 8mm DIAMETER HOLES THROUGH VEHICLE WING AND KITZ FLANGE AS SHOWN BELOW. (SEE 2 & 3)

- FIX SECTION INTO POSITION USING NUTS AND BOLTS SUPPLIED.

- CHECK FIXING POSITIONS FOR OVERLAP (SEE 1 & 4) AND REPEAT ABOVE.

- OFFER UP KITZ REAR SECTION AND REPEAT STEP 2. (SEE 5, 6 & 7).

- OFFER UP KITZ FRONT SECTION AND REPEAT STEP 2. (SEE 8 & 9).

PAINT FASTENINGS BOLTS AS REQUIRED, ANY TRIMMING NECESSARY CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.MER.A6

AXOR 2540

FRUNTZ KITZ

2. 175mm  FROM  CAB JOINT. 40mm UP INTO VEHICLE.

1. CENTRAL IN GAP. 10mm IN TO SPRAY PANEL.

3. 175mm FROM CAB JOINT, 40mm UP INTO VEHICLE.

8. 70mm DOWN. 25mm INTO WING.

5. 70mm BELOW TOP OF REAR WING. 20mm FROM WING EDGE.

6. CENTRAL BETWEEN FIXINGS 5 & 7.

7. 50mm UP FROM BOTTOM OF REAR SECTION. 40mm FROM WING EDGE.

9. 60mm UP FROM BOTTOM, 25mm INTO WING.

4. 20mm FROM REAR OF SPATZ FLANGE, 20mm BELOW CAB WING