NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- ON THE MAIN SECTION INSERT THE REAR FLAT PIECE FIRST (A) AND THEN PUSH UP FIRMLY THE FRONT HALF (B) UNTIL THE FLANGE CLICKS INTO PLACE.

- (3mm PILOT HOLES RECOMMENDED AND CHECK POSITION) THEN DRILL 3 No. 8mm DIAMETER HOLES THROUGH VEHICLE WING AND KITZ FLANGE AS SHOWN BELOW. (SEE 1, 2 & 3)

- FIX SECTION INTO POSITION USING NUTS AND BOLTS SUPPLIED.

- CHECK FIXING POSITIONS FOR OVERLAP (SEE 1 & 4) AND REPEAT ABOVE.

- OFFER UP KITZ REAR SECTION AND REPEAT STEP 2. (SEE 5 & 6).

- OFFER UP KITZ FRONT SECTION AND REPEAT STEP 2. (SEE 7 & 8).

PAINT FASTENINGS BOLTS AS REQUIRED, ANY TRIMMING NECESSARY CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.MER.A7

AXOR 1823

FRUNTZ KITZ

2. 175mm  FROM  CAB JOINT. 35mm UP INTO VEHICLE.

1. 110mm UP FROM BOTTM OF WING & 35mm INTO WING

3. 175mm FROM CAB JOINT, 35mm UP INTO VEHICLE.

7. 50mm DOWN. 30mm INTO WING.

5. 50mm BELOW TOP OF REAR WING. 35mm FROM WING EDGE.

A. INSERT THIS SIDE FIRST

6. 150mm UP FROM BOTTOM OF REAR SECTION. 35mm FROM WING EDGE.

8. 80mm UP FROM BOTTOM, 35mm INTO WING.

4. 50mm IN FROM RIGHT HAND EDGE & 30mm DOWN FROM END OF SLOPE

B. PUSH THIS SIDE UP UNTIL IT CLICKS IN TO PLACE SECOND