NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

- CLAMP CORRECTLY SIDED KITZ FORWARD SECTION TO THE INSIDE OF THE CAB MUDGUARD AS SHOWN BELOW.

- DRILL 3 No. 8mm DIAMETER HOLES AS INDICATED BELOW, (POSITIONS 1,2 & 3) 25mm INTO VEHICLE MUDGUARD PANEL THROUGH THE VEHICLE MUDGUARD AND THE KITZ FLANGE.  NOTE: CHECK PILOT HOLE POSITION 1 BEFORE ENLARGING.

- BOLT FRONT SECTION INTO PLACE WITH NUTS AND BOLTS SUPPLIED.

- OFFER UP REAR SECTION OF KITZ AND DRILL 3 No. 8mm HOLES EVENLY SPACED, (POSTIONS 4,5 & 6) AS SHOWN BELOW.

- BOLT REAR SECTION INTO PLACE USING NUTS AND BOLTS SUPPLIED.

PAINT BOLT HEADS IF REQUIRED.  ANY TRIMMING NECESSARY CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.REN.02

RENAULT PREMIUM

KITZ

1.  8mm HOLE 50mm UP FROM BOTTOM OF WING. CHECK PILOT HOLE.

2.   CENTRALLY BETWEEN 1 & 3.

3.  50mm FROM REAR OF WING.

4.   50mm DOWN FROM STEP IN CHASSIS WING.

5.  CENTRAL POSITION BETWEEN 4 & 5.

6.  75mm UP FROM BOTTOM OF KITZ REAR SECTION.