NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

IMPORTANT INFO: STREAMLINE SCANIA’S WERE NOT ORIGINALLY DESIGNED TO RUN WITH SUPER-SINGLE WHEELS ON THE STEER AXLE.  IN ADVERSE CONDITIONS IT IS POSSIBLE FOR THE TOP OF THE TYRE TO CATCH ON THE BOTTOM OF THE STREAMLINE CAB WING.  IF THIS IS THE CASE, THE TYRE WILL WEAR THE SPATZ KIT AWAY.  IT IS RECOMMENDED THAT 10mm IS REMOVED FROM THE BOTTOM OF THE STREAMLINE CAB WING (STRAIGHT AND RADIUS LOCATIONS 1-5 BELOW) PRIOR TO FITMENT OF THE SPATZ KITZ.

IF THE SPATZ KITZ ARE FITTED PRIOR TO ANY TRIMMING, BY DRILLING THE HOLES 45mm UP INTO THE VEHICLE (AS BELOW) IT WILL BE POSSIBLE TO USE THE SAME HOLES IN THE VEHICLE AND REPOSITION THE HOLES (DOWN 10mm) IN THE KITZ FLANGE SHOULD IT BE DISCOVERED THAT THE TYRES CATCH THE UNDERSIDE OF THE KITZ.  THIS MODIFICATION MUST BE CARRIED OUT AT THE FIRST SIGN OF ANY WEAR OF THE KITZ.

- CLAMP CORRECTLY SIDED KITZ FRONT SECTION TO THE INSIDE OF THE VEHICLE AS SHOWN BELOW.

- DRILL 5No.PILOT HOLES AS INDICATED APPROX 45mm UP FROM BOTTOM OF THE CAB VALANCE.  THROUGH CAB AND KITZ FRONT SECTION.

- CHECK POSITION AND THEN ENLARGE BOTH CAB WING AND SPATZ FLANGE HOLES TO 8mm.

- SECURE FRONT SECTION INTO PLACE USING NUTS AND BOLTS SUPPLIED.

- OFFER KITZ REAR SECTION TO INSIDE OF VEHICLE AS SHOWN BELOW.  ADJUST TO LINE UP WITH FRONT SECTION.  CLAMP INTO POSITION.

- DRILL 3No. 8mm HOLES AS SHOWN.

- SECURE INTO POSITION USING NUTS AND BOLTS SUPPLIED.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.SCA.02

SCANIA STREAMLINE

FITTING

INSTRUCTIONS

8. SHOULD BE 75mm UP FROM BOTTOM OF MUDWING.

7. EQUALLY SPACED BETWEEN 6 & 8.

6. 50mm ABOVE CREASE IN CHASSIS WING.

5. 10mm HOLE DRILLED 50mm IN FROM BACK END OF CAB.

4. CENTRAL ABOVE LOGO

3.EQUALLY SPACED BETWEEN 2 & 4.

2. 10mm HOLE AT TOP OF CURVE.

1. 10mm HOLE DRILLED 65     mm UP FROM BOTTOM OF KITZ FRONT