NOTE: CARE SHOULD BE TAKEN IN POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS RECOMMENDED.

1.SCANIA SERIES 4 ARE NOT SIDED.  CLAMP KITZ TO THE INSIDE OF VEHICLE AS SHOWN BELOW.

2.DRILL 6 No. 10 mm DIAMETER HOLES AS INDICATED APPROX 30mm INTO THE BOTTOM OF THE CAB VALENCE.

3.REMOVE KIT AND PUT A 9mm STUD THROUGH EACH HOLES IN THE CAB VALENCE, RETAINING WITH A PLASTIC WASHER.

4. ENLARGE HOLES IN KITZ FLANGE TO 13mm.

5.USING A FASTENER RECEPTACLE AS A TEMPLATE, DRILL 1 No. 3mm HOLE ON EACH SIDE OF THE SIX 13mm DIAMETER HOLES IN THE KITZ.

6. FIX EACH RECEPTACLE TO THE BACK OF THE KITZ FLANGE USING 2 No. 3mm X 10mm POP RIVETS.

7.OFFER KITZ UP TO VEHICLE AND SECURE BY TURNING EACH OF THE QUARTER TURN FASTENERS UNTIL LOCKED.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

NOTE:  THESE KITZ MUST BE REMOVED PRIOR TO REMOVING FRONT WING PANEL.

ALL 10mm HOLES SHOULD BE APPROX 30mm INTO CAB MOUNTING.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

KTZ.SCA.04

SCANIA SERIES 4 KITZ

FITTING INSTRUCTIONS

5.  10mm HOLE DRILLED MID WAY BETWEEN 4 & 6.

6. 10mm HOLE DRILLED 70mm UP FROM BOTTOM OF KITZ.

3 & 4 DRILLED AT TOP OF CURVES SYMMETRICALLY EITHER SIDE OF MUDGUARD CLIP. 380mm APART

2. 10mm HOLE DRILLED MIDWAY BETWEEN 1 & 3.

1. 10mm HOLE DRILLED 70mm UP FROM BOTTOM OF KITZ.