NOTE. CARE MUST BE TAKEN IN THE POSITIONING OF THE HOLES TO AVOID UNNECESSARY DAMAGE TO THE VEHICLE. THE DRILLING OF A 3mm PILOT HOLE IS STRONGLY RECOMMENDED.

1. CLAMP CORRECTLY SIDED FRUNTZ TO THE INSIDE OF VEHICLE AS SHOWN BELOW.

2. DRILL 3 No 8mm DIAMETER HOLES (POS 1,2 & 3) APPROX 30mm UP FROM THE BOTTOM OF

THE CAB VALANCE AND ONE 8mm DIAMETER HOLE (POS 4) 40mm INTO CAB VALANCE AS

SHOWN BELOW.

3. BEFORE FITTING FRUNTZ SECTION OFFER UP REAR SECTION.

4. DRILL 3 No 8mm HOLES (POS 5,6 & 7) 25mm INTO VEHICLE MUDGUARD.

5. USING THE SHORTER NUTS AND BOLTS, IN POSITIONS 1,2,3,5,6,7 AND LONGER IN POSITION

4, FASTEN BOTH REAR AND FRUNTZ SECTION INTO POSITION.

ANY TRIMMING REQUIRED CAN BE ACHIEVED USING AN ORDINARY HAND SAW OR STANLEY KNIFE.

# Text boxes

# SPATZ SHOP

SALES LINE

01527 60606

## KTZ.VOL.01

VOLVO FH KITZ

FITTING

INSTRUCTIONS

1. 8mm HOLE DRILLED 30mm IN FROM REAR OF FRUNTZ

2. 8mm HOLE DRILLED 310mm BEHIND CAB JOINT 30mm UP.

3. 8mm HOLE DRILLED 240mm IN FRONT OF CAB JOINT 30mm UP.

5. UNDER FRUNTZ SECTION 50mm ABOVE TOP CREASE IN REAR PART OF MUDWING.

6. APPROX 300mm ABOVE POSITION 7.

7. 50mm UP FROM BOTTOM OF KITZ REAR SECTION.

4. 8mm HOLE DRILLED 75mm UP FROM BOTTOM OF FRUNTZ 40mm INTO CAB VALANCE.

GREAT CARE SHOULD BE TAKEN DRILLING THIS POSITION. A PILOT HOLE IS STRONGLY ADVISED. ONCE DRILLED, REMOVE FRUNTZ AND SEE LOCATION OF THE HOLE IN FLANGE. LONG BOLT TO BE USED HERE.