Brackets

| Description | Part number | Quantity |
| --- | --- | --- |
| L shape bracket |  | 2 |
| Aluminium steps |  | 2 |
| Fibreglass drilling jig |  | 1 |

Passenger side:

Step 1: Take off the factory fitted indicator brackets!

Step 2: Fit the 4 x M8 nut inserts in the tank steps, in the holes pointed in the below photo, enlarging the pointed holes to 11.2mm diameter holes;

Step 3: Fix the “Fibreglass Side Skirt” drilling through mud wing and “Fibreglass Side Skirt” 8.5mm holes, using:

- 4 - M8 x 30mm bolts;

- 4 - M8 x 25mm washers fibreglass side skirt;

- 4 – M8 x 30mm washers on the mud wing;

- 4 - M8 nylock;

Step 4: Fix the “Aluminium steps” in to the M8 nut insets fitted in “Step 1”, using:

- 4 - M8 x 25mm Domehead;

- 4 - M8 x 25 washers;

Step 5: Place the indicators in the rectangular cut outs of the “Fibreglass Side Skirt”!

Driver side:

Step 1: Take off the factory fitted indicator rear bracket and unplug the heat shield indicator!

Step 2: Take off the pointed bolts in the bellow photo, located on the rear side of the heat shield and fit the “L shape bracket”, using:

- 2 – M8 x 30mm bolt;

- 2 – M8 x 25mm washer.

Step 3: Place the “Fibreglass drilling jig” over the heat shield, mark the three holes; drill 13mm holes through the marked holes.

Step 4: Fix the “Fibreglass Side Skirt” through the holes drilled at the “Step 3” and the brackets fixed at “Step 2”, using:

- 5 – M8 x 30mm washers;

- 5 – M8 nylocks.

Step 5: Fix the rear side of the “Fibreglass Side Skirt” drilling through mud wing and side skirt 8.5mm holes, using:

- 4 - M8 x 30mm bolts;

- 4 - M8 x 25mm washers “Fibreglass Side Skirt”;

- 4 – M8 x 30mm washers on the mud wing;

- 4 - M8 nylock;

Attention!!  Tight all the fixings!